## Slide 1
20 cm diameter spherical array
32 x RCF 2” 30W Neodymium Full-Range speakers Total power 32 x 30 = 960 W
Demonstration of a spherical source with 32 loudspeakers
By Angelo Farina and Lorenzo Chiesi
Low cost hand crafted prototype made by wood
Sphere obtained gluing a couple of IKEA bowls
32 channels portable class-D amplifier packed in a light 3U trolley
Orion USB 32ch interface
1500W, 18 kg
8x32 FIR filter matrix
Realtime, CPU load: < 6%
Can send up to 8 different signals in sharp beams pointed in arbitrary directions
The patterns are high order cardioids (up to 7th order)
DEMO 1
The beam is always pointing in frontal direction
Moving the selector, the cardioid order changes from 0 (omni) to 7
Notes: 1-Passando ad una formulazione matriciale più compatta
2-È possibile calcolare direttamente la soluzione ai minimi quadrati mediante l’espressione mostrata, modificata inserendo:Un ritardo di causalizzazione e un termine di regolarizzazione.
3-In particolare è stata utilizzata la regolarizzazione di Kirkeby con parametro di regolarizzazione variabile in frequenza.
4-Questo consente di ottenere una accurata inversione in banda mentre impedisce che il denominatore si annulli in alta e bassa frequenza
dove lo spettro delle risposte all’impulso del sistema tende a zero
5-Antitrasformando la matrice delle funzioni di trasferimento si determinano i coefficienti dei filtri FIR

## Slide 2
20 cm diameter spherical array
32 x RCF 2” 30W Neodymium Full-Range speakers Total power 32 x 30 = 960 W
Demonstration of a spherical source with 32 loudspeakers
By Angelo Farina and Lorenzo Chiesi
Low cost hand crafted prototype made by wood
Sphere obtained gluing a couple of IKEA bowls
32 channels portable class-D amplifier packed in a light 3U trolley
Orion USB 32ch interface
1500W, 18 kg
16x32 FIR filter matrix
Realtime, CPU load: < 10%
Can send 16 different signals in sharp beams pointed in 16 directions
The patterns are high order cardioids (5th order)
DEMO 2
The 16 beams are pointing all around in 22.5° steps
Moving the selector, the input is routed to one of these beams
Notes: 1-Passando ad una formulazione matriciale più compatta
2-È possibile calcolare direttamente la soluzione ai minimi quadrati mediante l’espressione mostrata, modificata inserendo:Un ritardo di causalizzazione e un termine di regolarizzazione.
3-In particolare è stata utilizzata la regolarizzazione di Kirkeby con parametro di regolarizzazione variabile in frequenza.
4-Questo consente di ottenere una accurata inversione in banda mentre impedisce che il denominatore si annulli in alta e bassa frequenza
dove lo spettro delle risposte all’impulso del sistema tende a zero
5-Antitrasformando la matrice delle funzioni di trasferimento si determinano i coefficienti dei filtri FIR

## Slide 3
20 cm diameter spherical array
32 x RCF 2” 30W Neodymium Full-Range speakers Total power 32 x 30 = 960 W
Demonstration of a spherical source with 32 loudspeakers
By Angelo Farina and Lorenzo Chiesi
Low cost hand crafted prototype made by wood
Sphere obtained gluing a couple of IKEA bowls
32 channels portable class-D amplifier packed in a light 3U trolley
Orion USB 32ch interface
1500W, 18 kg
16x32 FIR filter matrix
Realtime, CPU load: < 11%
Creates 16 virtual loudspeakers with directivities corresponding to spherical harmonics up to 3rd order (FuMa)
DEMO 3
HOA Encoding of two directive virtual sources
The sources can be rotated with Ambix-Encoder
The resulting 16-channels HOA signal is sent to the 16x32 beamforming filter matrix
The 32 channels feed the spherical loudspeaker array
Notes: 1-Passando ad una formulazione matriciale più compatta
2-È possibile calcolare direttamente la soluzione ai minimi quadrati mediante l’espressione mostrata, modificata inserendo:Un ritardo di causalizzazione e un termine di regolarizzazione.
3-In particolare è stata utilizzata la regolarizzazione di Kirkeby con parametro di regolarizzazione variabile in frequenza.
4-Questo consente di ottenere una accurata inversione in banda mentre impedisce che il denominatore si annulli in alta e bassa frequenza
dove lo spettro delle risposte all’impulso del sistema tende a zero
5-Antitrasformando la matrice delle funzioni di trasferimento si determinano i coefficienti dei filtri FIR